## Slide 1: Photodetection in KM3NeT
Uli Katz
ECAP / Univ. Erlangen
APPEC Technology Forum 2015 Low Light-Level Detection in Astroparticle Physics and in Medical Applications 22+23 April 2015, Munich, Germany

## Slide 2: The plan for the next 30 minutes:
The KM3NeT project: Concept and overview
Light detection in KM3NeT
Prototype results
Timelines
Summary

## Slide 3: The KM3NeT project: Concept and overview

## Slide 4: How does a neutrino telescope work?
Neutrino interacts in the (vicinity of the) telescope
Charged secondaries cross the detector volume (water or ice) and stimulate Cherenkov emission
Recorded by a 3D-array of photo-sensors
Neutrino energy range : few GeV – above PeV (depends on density of instrumentation)

## Slide 5: The KM3NeT Collaboration

## Slide 6: The KM3NeT DOM
31 3-inch PMTs in 17-inch glass sphere (cathode area~ 3x10-inch PMTs)
  19 in lower, 12 in upper hemisphere
  Suspended by plastic structure
31 PMT bases (total ~140 mW) (D)
Front-end electronics (B,C)
Al cooling shield and stem (A)
Single penetrator
Advantages:
  Increased photocathode area
  1-vs-2 photo-electron separation  better sensitivity to coincidences
  Directionality
  Cost / photocathode area
A
B
C
C
D
PMT

## Slide 7
Mooring line:
  Buoy (syntactic foam)
  2 pre-stretched Dyneema© ropes (4 mm diameter)
  18 storeys (one DOM each)
Electro-optical backbone (VEOC):
  Flexible hose ~ 6mm diameter
  Oil-filled
  Fibres and copper wires
  At each storey: connection to 1 fibre + 2 wires
  Break-out box with fuses at each storey: One single pressure transition
KM3NeT detection units (DUs)

## Slide 8: The building block concept
Building block:
  115 detection units
  Segmentation enforced by technical reasons
  Large block (neutrino astronomy)
  Sensitivity for muons independent of block size above ~75 strings
  One block ~ half IceCube
Small block (neutrino oscillations)
      Precision measurement of atmospheric neutrinos
      One block ~ 6 Mtons
  Allows for staged, block-wise, multi-site installation
DU distance adjusted to scientific objective: 90-120 m for neutrino astronomy / 20 m for oscillation research

## Slide 9: ARCA and ORCA
ARCA =
Vertical OM distance = 36 m
ORCA =
Vertical OM distance = 6 – 12 m
Astroparticle
Research with
Cosmics in the
Abyss
Oscillation
Research with
Cosmics in the
Abyss
+

## Slide 10: KM3NeT development
Phase | Blocks/ strings | Primary deliverables / site(s) | PMTs needed
1 | 0.2/31 | Proof of feasibility and first science results; KM3NeT-Fr + KM3NeT-It sites | 18.000
2.0 | 2/230 | Measurement of neutrino signal reported by IceCube; All-flavor neutrino astronomy; KM3NeT-It site | +175.000
 | 1/115 | Neutrino mass hierarchy; KM3NeT-Fr site | 
3 | 6+1/805 | Neutrino astronomy including Galactic sources; Multiple sites | +260.000

## Slide 11: KM3NeT resolutions
Track-like events: Cascades:
ne CC events with containment cut
1°
2°
Muon energy: d(log10 E)=0.25-0.3 at E > 10 TeV
Cascade energy: 5-10% at E > some 10 TeV
All-flavour neutrino astronomy in reach

## Slide 12: KM3NeT science objectives
All-flavour neutrino astronomy
Precision measurements in neutrino physics
Nodes for earth and sea science research

## Slide 13: Light detection in KM3NeT

## Slide 14: KM3NeT readout
HV for PMTs
Discrimination w.r.t. predefined threshold
31 PMTs + bases
2 octopus boards
Power board
Signal collection
FPGA for TDC (time & time over threshold), time stamping (1 ns precision);
Interface for time synchronisation:
Control of calibration devices; Communication;
Online filter
on shore
All data
to shore
(optical
Fibres)
Central Logic Board (CLB)

## Slide 15: Implementation in DOM
Reflective rings around PMTs (+27% light detection, see JINST 8 (2013) T03006)
PMTs supported by plastic structure produced by 3D-printing
Calibration: Acoustic sensor and compass + tiltmeter
Electronics components attached to cooling structure
One single penetrator for connection to vertical cable

## Slide 16: PMT specifications
Parameter | Requirement
Photocathode diameter | > 72 mm
Nominal Voltage for Gain 3x106 | 900 – 1300 V
Gain slope = log10(gain)/log10(HV) | 6.5 – 8.0
QE at 404 nm | > 23 %
QE at 470 nm | > 18 %
TTS (FWHM) | < 5 ns
Dark count rate (0.3 p.e. threshold) | < 2 kHz
Pre-pulses | < 1 %
Delayed pulses | < 3.5 %
Early afterpulses | < 2 %
Late afterpulses | < 10 %

## Slide 17: PMTs available
ETEL D792
Hamamatsu R12199
HZC XP53B20
  
Fulfil specifications; orders placed / expected
First prototype not yet compliant with specifications (gain, dark rate, afterpulses, …), further development under way
Note: In all cases price/photocathode area < 10-inch tubes (MELZ?)
+MELZ …

## Slide 18: Some results of PMT measurements: QE …
Note: These are “normal”, i.e. not super- or hyper-bialkali PMTs
Hamamatsu

## Slide 19: … and TTS
All measurements for ETEL & Hamamatsu within specifications
Hamamatsu
Hamamatsu

## Slide 20: Prototype results

## Slide 21
K40 coincidence rate  PMT efficiencies
g
g
Up to 150 Cherenkov photons
per decay
e- (β decay)
40K
40Ca
Concentration of 40K is stable
(coincidence rate ~5 Hz on adjacent PMTs)
DOM prototype (PPM-DOM)
Coincidence rate on 2 adjacent PMTs
(33°angular separation)
Peak position  time offsets
Eur.Phys.J. C74 (2014) 3056
Deployed at
ANTARES in
April 2013

## Slide 22
PPM-DOM: Atmospheric Muons
Number of coincident hits in a DOM
Zenith angle of hit PMTs in events with more than 7 coincident hits
>5 coincidences within 20ns ⇒ reduced K40 contribution,
dominated by atmospheric muons
More upper PMTs in multi-hit events ⇒
directional information
from single storey
Eur.Phys.J. C74 (2014) 3056

## Slide 23
DU mini-prototype (PPM-DU): 3 DOMs
Deployed at
KM3NeT-It
in May 2014

## Slide 24
PPM-DU: Inter-DOM timing
K40 coincidence rate as a function of the angle between PMTs. Note: Different PMT types!
Relative timing calibration of 31 PMTs in DOM using coincidences.
Note: Extremely stable over many runs

## Slide 25
PPM-DU: Intra-DOM timing
Calibration with pulsed LED
Time difference – light travel time = Signal travel time
Result very stable over several months, RMS of jitter < 1 ns

## Slide 26
PPM-DU: Muon reconstruction
Reconstruct muon trajectory from hits on 3 DOMs
Ambiguities can be reduced by cuts on time differences
7° FWHM resolution achieved

## Slide 27: Timelines

## Slide 28: KM3NeT time lines and funding
Phase | Invest/M€ | Time lines | Funding
1 | 31 | 2014-16: Construction (24 ARCA- and 6 ORCA-DUs) | secured
2.0 | +55 | 2015: ESFRI proposal (decision 2016) 2016-20: Construction 2022: Physics results | applications pending
 | +40 |  | 
3 | +100-120 | After 2020 | to be defined

## Slide 29: Summary

## Slide 30: Summary and outlook
KM3NeT is a future multi-site research infrastructure in the Mediterranean Sea
Priority science goals:
    All-flavour neutrino astronomy
    Measurement of the neutrino mass hierarchy
Light detection using multiple 3-inch PMTs per optical module
    Concept technically proven
    Prototypes and simulations show high potential
  KM3NeT construction has started (Phase-1), next phase (ARCA & ORCA) to follow in 2016-20
Stay tuned!